中国合格评定国家认可委员会

认 可 证 书 附 件

（注册号：CNAS L5142）

名称:浙江生辉照明有限公司测试中心

地址：浙江省嘉兴市秀洲工业区加创南路

认可依据：ISO/IEC 17025:2005、EPA能源之星以及CNAS特定认可要求

签发日期：2014年06月29日         有效期至：2017年06月28日

更新日期：2014年06月29日

附件4  认可的“能源之星”检测能力范围

| 序号 | 检测 对象 | 项目/参数 | 领域 代码 | 检测标准（方法）名称及编号（含年号） | 限制 范围 | 说明 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 序号 | 名称 |  |  |  |  |
| 1 | 普通照明用自镇流灯 | 1 | 全部项目 | 0437 | 普通照明用自镇流灯的安全要求 GB 16844-2008 IEC 60968-2012 |  |  |
|  |  | 2 | 全部项目 | 0438 | 普通照明用自镇流荧光灯的性能要求 GB/T 17263-2002 IEC 60969-2001 |  |  |
| 1 | 普通照明用自镇流灯 | 3 | 全部项目 | 0437 | 普通照明用50V以上自镇流LED灯 安全要求 GB 24906-2010 IEC 62560-2011 |  |  |
|  |  | 4 | 全部项目 | 0438 | 普通照明用自镇流LED灯性能要求 GB/T 24908-2010 |  |  |
|  |  | 5 | 寿命测试 | 0438 | 紧凑型荧光灯寿命测试方法 IES LM-65-2001 |  |  |
|  |  | 6 | 光电测试 | 0438 | 固态照明产品电学和光学参数测量方法 IES LM-79-2008 |  |  |
|  |  | 7 | 部分项目 | 0438 | 能源之星一体式LED灯规范V1.4 | 不测噪音和瞬态保护 |  |
| 2 | 普通照明用LED模块 | 1 | 全部项目 | 0437 | 普通照明用LED模块 安全要求 GB 24819-2009 IEC 62031-2008 |  |  |
|  |  | 2 | 全部项目 | 0438 | 普通照明用LED模块 性能要求 GB/T 24823-2009 | 不测“灯座/连接器”、和“电磁兼容” |  |
|  |  | 4 | 寿命测试 | 0438 | LED 光源流明维持测量方法 IES LM-80-2008 |  |  |
| 3 | 灯的控制装置 | 1 | 全部项目 | 0437 | 灯的控制装置 第1部分：一般要求和安全要求 GB 19510.1-2009 IEC 61347-1：2010 |  |  |
|  |  | 2 | 全部项目 | 0437 | 灯的控制装置 第14部分：LED模块用直流或交流电子控制装置的特殊要求 GB 19510.14-2009 IEC 61347-2-13：2006 |  |  |
|  |  | 3 | 部分项目 | 0438 | LED模块用直流或交流电子控制装置性能要求 GB/T 24825-2009 IEC 62384-2006 | 不测： 声频阻抗 |  |
| 4 | 灯具 | 1 | 部分项目 | 0437 | 灯具 第1部分：一般要求与测试 GB 7000.1-2007 IEC 60598-1：2008 | 不测： 紫外线辐射 |  |
|  |  | 2 | 部分项目 | 0437 | 灯具 第2-1部分：特殊要求 固定式通用灯具 GB 7000.201-2008 IEC 60598-2-1 1979+A1：1987 | 不测：IPX1 |  |
|  |  | 3 | 部分项目 | 0437 | 灯具 第2-2部分：特殊要求 嵌入式灯具 GB 7000.202-2008 IEC 60598-2-2：2011 | 不测：IPX1 |  |
| 4 | 灯具 | 4 | 部分项目 | 0437 | 灯具 第2-13部分：特殊要求 地面嵌入式灯具 GB 7000.213-2008 IEC 60598-2-13：2006 | 不测：IPX1，耐静负荷、抗扭矩和剪力负荷、机械强度 |  |
|  |  | 5 | 部分项目 | 0437 | 灯具 第2-18部分：特殊要求 游泳池和类似场所用灯具 GB 7000.218-2008 IEC 60598-2-18：1993 | 不测：IPX1、耐久性试验和热试验 |  |
|  |  | 6 | 部分项目 | 0437 | 道路与街道照明灯具安全要求 GB 7000.5-2005 IEC 60598-2-3：2002+A1：2011 | 不测： IPX1和风压 |  |
| 4 | 灯具 | 7 | 部分项目 | 0437 | 投光灯具安全要求 GB 7000.7-2005 IEC 60598-2-5：1998 | 不测：IPX1 |  |
|  |  | 8 | 部分项目 | 0438 | 道路照明用LED性能要求 GB/T 24907-2010 | 不测： 电磁兼容 |  |
|  |  | 9 | 光度测量 | 1615 | 灯具分布光度测量的一般要求 GB/T 9468-2008 |  |  |
| 5 | 照明电器产品 | 1 | 低温试验 | 43101 | 电工电子产品环境试验第2部分：试验方法 试验A：低温 GB/T 2423.1-2008 | 只测： 体积≤0.67m³ 温度范围： -40℃～0℃ |  |
|  |  | 2 | 高温试验 | 43102 | 电工电子产品环境试验第2部分：试验方法 试验B：高温 GB/T 2423.2-2008 | 只测： 体积≤0.67m³ 温度范围： 0℃～150℃ |  |
|  |  | 3 | 恒定湿热试验 | 43103 | 电工电子产品环境试验第2部分：试验方法 试验Cab：恒定湿热试验 GB/T 2423.3-2006 | 只测： 体积≤0.67m³ 温度范围： 20℃～85℃ 湿度范围： RH85%～RH95% |  |
| 5 | 照明电器产品 | 4 | 温度变化试验 | 43104 | 电工电子产品环境试验第2部分：试验方法 试验N：恒温度变化 GB/T 2423.22-2012 | 只测： 方法Na,Nb 体积≤0.67m³ 温度范围： -45℃～150℃ 温度变化率： ≤5℃/min |  |
|  |  | 5 | 盐雾试验 | 43117 | 人造气氛腐蚀试验 盐雾试验 GB/T 10125-2012 | 只测： 中性盐雾 |  |

CHINA NATIONAL ACCREDITATION SERVICE FOR CONFORMITY ASSESSMENT

APPENDIX OF ACCREDITATION CERTIFICATE

(Registration No. CNAS L5142)

NAME:Test Center of Zhejiang Shenghui Lighting Co., Ltd.

ADDRESS:Jiachuang South Road, Xiuzhou Industrial Park, Jiaxing, Zhejiang, China

Accreditation Criteria:ISO/IEC 17025:2005 , requirements of EPA ENERGY STAR® Program and relevant requirements of CNAS

Date of Issue:2014-06-29                      Date of Expiry:2017-06-28

# Date of Update：2014-06-29

APPENDIX 4   ACCREDITED ENERGY STAR TESTING

| № | Test Object | Item/Parameter | Code of Field | Title, Code of Standard or Method | Limitation | Note |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | № | Item/ Parameter |  |  |  |  |
| 1 | Self-ballasted lamps for general lighting Service | 1 | All Items | 0437 | Self-ballasted lamps for general lighting services safety requirement GB 16844-2008 IEC 60968:2012 |  |  |
|  |  | 2 | All Items | 0438 | Self-ballasted lamps for general lighting Service-Performance requirements GB/T 17263-2002 IEC 60969-2001 |  |  |
| 1 | Self-ballasted lamps for general lighting Service | 3 | All Items | 0437 | Self-ballasted LED lamps for general lighting services＞50V—Safety specifications GB 24906-2010 IEC 62560-2011 |  |  |
|  |  | 4 | All Items | 0438 | Self-ballasted LED lamps for general lighting services—Performance requirements GB/T 24908-2010 |  |  |
|  |  | 5 | Life Test | 0438 | Life Testing of Compact Fluorescent Lamps IES LM-65-2001 |  |  |
| 1 | Self-ballasted lamps for general lighting Service | 6 | Electrical and Photometric Measurements | 0438 | Electrical and Photometric Measurements of Solid-State Lighting Products IES LM-79-2008 |  |  |
|  |  | 7 | Part of Items | 0438 | ENERGY STAR Program Requirements for Integral LED Lamps Eligibility Criteria-Version 1.4 | Except for Audible Noise and Transient Protection |  |
| 2 | LED modules | 1 | All Items | 0437 | LED modules for general lighting - Safety specifications GB 24819-2009 IEC 62031-2008 |  |  |
|  |  | 2 | Part of Items | 0438 | LED modules for general lighting - Performance requirements GB/T24823-2009 | except for：“lamppholer/connector”and “Electromagnetic compatibility” |  |
|  |  | 4 | Life Test | 0438 | Measuring Lumen Maintenance of LED Light Sources IES LM-80-2008 |  |  |
| 3 | Lamp controlgear | 1 | All Items | 0437 | Lamp controlgear –part 1:General and safety requirements GB 19510.1—2009 IEC 61347-1：2010 |  |  |
| 3 | Lamp controlgear | 2 | All Items | 0437 | Lamp controgear-Part2-14: Particular requirements for d.c. or a.c. supplied electronic controlgear for LED modules GB 19510.14-2009 IEC 61347-2-13：2006 |  |  |
|  |  | 3 | Part of Items | 0438 | DC or AC supplied electronic control gear for LED modules-Performance requirements GB/T 24825-2009 IEC 62384-2006 | Except for Acoustic impedance |  |
| 4 | Luminaire | 1 | Part of Items | 0437 | Luminaires General requirements and tests GB 7000.1-2007 IEC 60598-1：2008 | Except for IPX1、 Ultraviolet radiation |  |
|  |  | 2 | Part of Items | 0437 | Luminaires—part2-1:Particular requirements—Fixed general purpose luminaires GB 7000.201-2008 IEC 60598-2-1:1979+A1:1987 | Except for IPX1 |  |
| 4 | Luminaire | 3 | Part of Items | 0437 | Luminaires - Part 2-2: Particular requirements - Recessed luminaries GB7000.202-2008 IEC60598-2-2:2011 | Except for IPX1 |  |
|  |  | 4 | Part of Items | 0437 | Luminaires - Part 2-13: Particular requirements - Ground recessed luminaries GB 7000.213-2008 IEC 60598-2-13:2006 | Except for IPX1、Hydrostatic load 、Anti torque and Shear load 、Mechanical strength |  |
| 4 | Luminaire | 5 | Part of Items | 0437 | luminaires-part2-18 Particular requirements-luminaires for swimming pools and similar application GB 7000.218-2008 IEC 60598-2-18:1993 | Except for IPX1、Endurance test and Thermal test |  |
|  |  | 6 | Part of Items | 0437 | Safety requirements of luminaires for road and street lighting GB7000.5-2005 IEC60598-2-3:2002+A1:2011 | Except for IPX1、wind speeds |  |
| 4 | Luminaire | 7 | Part of Items | 0437 | Safety requirements for floodlights GB 7000.7-2005 IEC60598-2-5:1998 | Except for IPX1 |  |
|  |  | 8 | Part of Items | 0438 | LED Lamps for road lighting-performance specifications GB/T 24907-2010 | Except for Electromagnetic compatibility |  |
|  |  | 9 | Photometry and goniophotometry Measurements | 1615 | General requirements for the photometry and goniophotometry of luminaries GB/T 9468-2008 |  |  |
| 5 | Electric and electronic products | 1 | Low Temp.Test | 043101 | Environmental testing for electric and electronic products-Part 2:Test methods-Tests A:Cold GB/T 2423.1-2008 | Accredited only for：Volume≤0.67m³ Temp.scope: -40℃～0℃ |  |
|  |  | 2 | High Temp.Test | 043102 | Environmental testing for electric and electronic products-Part 2:Test methods-Tests B:Dry heat GB/T 2423.2-2008 | Accredited only for：Volume≤0.67m³ Temp.scope： 0℃～150℃ |  |
| 5 | Electric and electronic products | 3 | Damp heatTest | 043103 | Environmental testing for electric and electronic products-Part 2:Testing method test Cab: Damp heat, Steady state GB/T 2423.3-2006 | Accredited only for：Volume≤0.67m³ Temp.scope： 20℃～85℃ Humidity scope:RH85%～RH95% |  |
|  |  | 4 | Temp. changeTest | 043104 | Environmental testing for electric and electronic products-Part 2:Test methods Test N: Change of temperature GB/T 2423.22-2012 | Accredited only for：Methods of Na,Nb Temp.scope ： -45℃～150℃ Rate of Temp. change≤ 5℃/min |  |
|  |  | 5 | Salt spray | 043117 | Corrosion tests in artificial atmospheres -- Salt spray tests GB/T 10125-2012 | Accredited only for：NSS |  |

中国合格评定国家认可委员会

认 可 证 书 附 件

（注册号：CNAS L5142）

名称: 浙江生辉照明有限公司测试中心

地址：浙江省嘉兴市秀洲工业区加创南路

认可依据：ISO/IEC 17025、EPA能源之星以及CNAS特定认可要求

签发日期：2015年10月20日         有效期至：2017年06月28日

附件4  认可的“能源之星”检测能力范围

| 序号 | 检测 对象 | 项目/参数 | 检测标准（方法）名称及编号（含年号） | 限制 范围 | 说明 |
| --- | --- | --- | --- | --- | --- |
|  |  | 序号 | 名称 |  |  |  |
| 1 | 一体式LED灯 | 1 | 部分项目 | 能源之星灯泡产品规格的合格标准要求V1.1 | 不测:噪音和瞬态保护 |  |
|  |  | 2 | 效能 | 固态照明产品电学和光学参数测量方法 IES LM-79-2008 |  |  |
|  |  | 3 | 光输出 |  |  |  |
|  |  | 4 | 中心光强 |  |  |  |
|  |  | 5 | 光强分布 |  |  |  |
|  |  | 6 | 流明维持 |  |  |  |
|  |  | 7 | 寿命 |  |  |  |
|  |  | 8 | 相关色温 |  |  |  |
|  |  | 9 | 显色指数 |  |  |  |
| 1 | 一体式LED灯 | 10 | 颜色维持 | 固态照明产品电学和光学参数测量方法 IES LM-79-2008 |  |  |
|  |  | 11 | 颜色角度均匀性 |  |  |  |
|  |  | 12 | 相关色温 | 色度学 CIE Pub. No. 15:2004 |  |  |
|  |  | 13 | 显色指数 | 光源显色性测量和表述方法 CIE Pub. No.13.3:1995 |  |  |
|  |  | 14 | 寿命，流明维持-高温寿命测试 | 能源之星灯泡产品规格V1.0 试验方法-高温寿命测试 |  |  |
|  |  | 15 | 寿命，流明维持-室温寿命测试 | 能源之星灯泡产品规格V1.0 试验方法-室温寿命测试 |  |  |
|  |  | 16 | 加温光输出比 | 能源之星灯泡产品规格V1.0 试验方法-加温光输出比 |  |  |
|  |  | 17 | 启动时间 | 能源之星灯泡产品规格V1.0 试验方法-启动时间 |  |  |

CHINA NATIONAL ACCREDITATION SERVICE FOR CONFORMITY ASSESSMENT

SCHEDULE OF ACCREDITATION CERTIFICATE

(Registration No. CNAS L5142)

NAME:Test Center of Zhejiang Shenghui Lighting Co., Ltd.

ADDRESS:Jiachuang South Road, Xiuzhou Industrial Park, Jiaxing, Zhejiang, China

Accreditation Criteria:ISO/IEC 17025, requirements of EPA ENERGY STAR® Program and relevant requirements of CNAS

Date of Issue:2015-10-20                      Date of Expiry:2017-06-28

SCHEDULE 4   ACCREDITED ENERGY STAR TESTING SCOPE

| № | Test Object | Item/Parameter | Title, Code of Standard or Method | Limitation | Note |
| --- | --- | --- | --- | --- | --- |
|  |  | № | Item/ Parameter |  |  |  |
| 1 | Integral LED Lamps | 1 | Part of Items | ENERGY STAR Program Requirements Product Specification for Lamps Eligibility Criteria Version 1.1 | Except for： noise and Transient protection |  |
|  |  | 2 | Efficacy | Electrical and Photometric Measurements of Solid-State Lighting Products IES LM-79-2008 |  |  |
|  |  | 3 | Light Output |  |  |  |
| 1 | Integral LED Lamps | 4 | Center Beam Intensity | Electrical and Photometric Measurements of Solid-State Lighting Products IES LM-79-2008 |  |  |
|  |  | 5 | Luminous Intensity Distribution |  |  |  |
|  |  | 6 | Lumen Maintenance |  |  |  |
|  |  | 7 | Lifetime |  |  |  |
|  |  | 8 | CCT |  |  |  |
|  |  | 9 | CRI |  |  |  |
|  |  | 10 | Color Maintenance |  |  |  |
|  |  | 11 | Color Angular Uniformity |  |  |  |
| 1 | Integral LED Lamps | 12 | CCT | COLORIMETRY CIE Pub. No.15：2004 |  |  |
|  |  | 13 | CRI | Method of Measuring and Specifying Color Rendering of Light Sources CIE Pub. 13.3:1995 |  |  |
| 1 | Integral LED Lamps | 14 | Lumen Maintenance-Elevated Temperature Life Test | ENERGY STAR Program Requirements Product Specification for Lamps Version 1.0 -Elevated Temperature Life Testing |  |  |
|  |  | 15 | Lumen Maintenance-Ambient Temperature Life Test | ENERGY STAR Program Requirements Product Specification for Lamps Version 1.0 -Ambient Temperature Life Testing |  |  |
|  |  | 16 | ETLOR | ENERGY STAR Program Requirements Product Specification for Lamps Version 1.0 –Elevated Temperature Life Light Output Ratio |  |  |
|  |  | 17 | Start Time | ENERGY STAR Program Requirements Product Specification for Lamps Version 1.0 - Start Time |  |  |