玩具和儿童用品检测领域认可能力范围

表述说明

# 1 目的和适用范围

为提高玩具和儿童用品检测领域实验室项目申请、现场评审的一致性和有效性，进一步规范该领域检测能力表述，促进CNAS认可结果更好地为相关方所理解和接受，CNAS秘书处根据CNAS-R01：2010《认可标识和认可状态声明管理规则》和CNAS-RL01：2011《实验室认可规则》制定本文件，对玩具和儿童用品检测领域认可能力范围表述给予说明。

本文件适用于检测和校准实验室对玩具和儿童用品领域检测项目申请、现场评审，以及实验室认可证书（附件）的能力范围表述。

# 2 能力范围表述要求

  - 检测对象

通常情况应依据实验室的实际检测范围表述为“玩具”、“儿童用品”或“玩具和儿童用品”，如检测标准仅适用于玩具，应明确填写“玩具”，如实验室的检测范围为单一产品，可表述具体的产品名称如“玩具车”、“儿童椅”等。

  - 项目/参数

- 当检测对象为“玩具”、“儿童用品”或“玩具和儿童用品”等时不宜用全部参数或部分参数进行概括表述；当检测对象为某种单一产品时，若检测标准与该产品相对应，可采用全部参数或部分参数的表述方式。

- 玩具和儿童产品领域的项目/参数可归纳为“机械和物理性能”、化学性能类参数、“燃烧性能”、“电性能”及其他参数。项目/参数应按照“机械和物理性能”、“燃烧性能”、化学性能类参数、“电性能”及其他参数的顺序排列。

注：其他参数应填写实际检测项目，在上述性能参数之后逐一列出。

- 化学性能类参数应根据具体检测项目进行展开，如“特定元素迁移：砷、钡、镉、铬、铅、汞、锑、硒”、“总铅”、“邻苯二甲酸盐含量”等。

  - 领域代码

领域代码应按照CNAS—AL06《实验室认可领域分类》进行填写。

  - 检测标准（方法）名称及编号（含年号）

    - 检测标准（方法）名称及编号（含年号）填写应包含标准编号、版本号、修正案及年号、标准名称等完整信息，并按照标准编号、版本号、修正案及年号、标准名称依次排列。

    - 对于同一个项目/参数，可依据多个检测标准，标准顺序宜按照国家标准、国际标准、欧洲标准、美国标准、澳/新标准、日韩标准等依次排列。

    - 对于同一个检测标准包含了多个项目/参数，应以项目/参数为参照基准，将该标准分别填写到与项目/参数对应的标准栏中。

    - 如两个或多个标准为等同采用关系，应将其置于同一单元格中；

    - 如某些技术法规引用检测方法标准时，应当把技术法规和相应的检测标准置于同一单元格中；

    - 如检测依据为实验室自制或非标准方法，表述应当包括该方法的编号及完整名称，并应在说明栏注明该方法为实验室自制方法或非标准方法。

    - 如检测标准（方法）与检测对象不对应，应按照实验室自制或非标准方法进行表述，并在限制范围中对检测标准（方法）的使用范围和对象进行限定。

  - 限制范围

    - 可用“只测”或“不测”对部分项目以及对检测量程和/或检测方法等方面进行限制。

    - 当使用“不测”时，对于检测标准（方法）的全部检测项目，应确保除“不测”的内容，实验室具备其余全部检测能力。

    - 应注明限制的具体项目及检测范围，如需对某些检测标准（方法）的部分条款进行限制，应注明被限制条款的条款号及具体名称，不宜只对条款号进行限制。

    - 如需对检测标准（方法）的某些条款下的内容进行限制，限制范围表述应包含该条款号、具体项目和受限内容。

  - 说明

应视具体情况注明移动设施、租用设备、扩项、变更、非标方法、特定客户等信息。

  - 特殊要求

对于某些管理机构对于认可能力的证明存在特殊要求的，如美国CPSC对ASTM F 963-11的能力表述提出了要求，建议将将项目/参数打开到具体的标准条款。打开标准条款时，将不同的条款归纳到可以对“机械及物理性能”、化学性能类参数、“燃烧性能”、“电性能”及其他参数的类别中。

# 3 玩具和儿童用品检测领域认可能力范围表述示例

3.1 中文表述示例

具体见附录A.1。

3.2 英文表述示例

具体见附录A.2。

# 附录A

# 玩具和儿童用品检测领域认可能力范围表述示例

# A.1中文表述示例

| 序号 | 检测 对象 | 项目/参数 | 领域 代码 | 检测标准（方法）名称及编号（含年号） | 限制 范围 | 说明 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 序号 | 名称 |  |  |  |  |
| 1 | 玩具 玩具 玩具 玩具 玩具 玩具 玩具 | 1 | 机械和物理性能 | 0327 | GB6675-2003+A1：2005附录A 国家玩具安全技术规范 附录A |  |  |
|  |  |  |  | 0327 | ISO 8124-1:2009 玩具安全-第1部分 物理和机械性能 AS/NZS ISO 8124.1:2002+ A1:2007 + A2:2009 澳大利亚/新西兰标准 玩具安全-第1部分：有关机械和物理性能的安全方面 |  |  |
|  |  |  |  | 0327 | EN 71-1:2011 玩具安全 第1部分 物理和机械性能 BS EN 71-1:2011 玩具安全 第1部分 物理和机械性能 |  |  |
|  |  |  |  | 0327 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.1材料， 4.5发声玩具， 4.6小零件， 4.7可触及边缘， 4.8 突出物， 4.9可触及尖端， 4.10金属丝或杆件， 4.11钉子和紧固件， 4.12 包装薄膜， 4.13.2 铰链， 4.14玩具中的绳子,带子和橡皮筋， 4.16有限空间， 4.17车轮,轮胎和轮轴，4.18孔、间隙及机械装置的可触及性， 4.19仿制防护装置， 4.20安抚奶嘴， 4.21 弹射玩具， 4.22出牙器和出牙用玩具，4.23摇铃， 4.24挤压玩具， 4.26可附在婴儿床或婴儿用围栏上的玩具， 4.27填充类玩具， 4.28婴儿小推车和婴儿车玩具， 4.31气球， 4.32带球形末端的玩具， 4.33 弹球， 4.34球， 4.35绒球， 4.36 半球形玩具， 4.38磁体， 4.39 下鄂可陷入的手柄和方向盘， 8.5正常使用， 8.6滥用测试， 8.7冲击测试， 8.8部件移除的扭力测试， 8.9部件移除的拉力测试， 8.10 压力测试， 8.11轮胎移除试验和咬接式轮轴组合的试验， 8.12挠曲测试， 8.14弹射玩具， 8.19发声玩具测试， 8.21 包装薄膜厚度， 8.22绳圈和绳索测试， 8.24 磁体测试， 8.25锁定装置或其他装置的测试方法 （……逐一列出机械物理性能的相关条款） |  |  |
|  |  | 2 | 燃烧性能 | 0327 | GB6675-2003+A1：2005附录B 国家玩具安全技术规范 附录B |  |  |
|  |  |  |  | 0327 | EN71-2:2011 玩具安全-易燃性能 | 不测：4.1 中易燃/高易燃和极易燃的气体及液体 |  |
|  |  |  |  | 0327 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.2 易燃性， A5 硬体和软体玩具的易燃性测试程序， A6 布料的易燃性测试程序 |  |  |
|  |  | 3 | 特定元素迁移：砷、钡、镉、铬、铅、汞、锑、硒 | 0244 | ISO 8124.3:2010 玩具安全 第3部分 特定元素的迁移 |  |  |
|  |  |  |  | 0244 | AS/NZS ISO 8124-3:2003 澳大利亚/新西兰标准 玩具安全- 第三部分：某些元素的转移 |  |  |
|  |  |  |  | 0244 | EN71-3:1994+A1:2000+AC:2002 玩具安全 第三部分：特定元素的迁移 |  |  |
|  |  |  |  | 0244 | ASTM F963-08 消费者安全规范：玩具安全 条款： 4.3.5 重金属 8.3重金属测试方法 |  |  |
|  |  | 4 | 总铅 | 0215 | CPSC-CH-E1001-08.1 美国消费品安全委员会实验室科学局化学部测试方法:儿童金属产品（包括儿童金属珠宝）中总铅测定的标准操作程序 |  |  |
|  |  |  |  | 0215 | CPSC-CH-E1002-08.1 美国消费品安全委员会实验室科学局化学部测试方法:儿童非金属产品中总铅测定的标准操作程序 |  |  |
|  |  |  |  | 0215 | ASTM E1613-04 用感应耦合等离子体原子发射光谱法(ICP-AES),火焰原子吸收光谱法(FAAS)或石墨炉原子吸收光谱技术(GFAAS)测定铅含量的标准试验方法 |  |  |
|  |  |  |  | 0215 | ASTM E1645-07 电炉加热或微波消解法测定干漆样本铅含量的方法 |  |  |
|  |  |  |  | 0215 | CPSC 16 CFR 1303美国消费品安全委员会美国联邦法规第16部分 CPSC-CH-E1003-09.1 美国消费品安全促进法:表面油漆及其类似涂层中铅含量测定标准操作程序 |  |  |
|  |  | 5 | 邻苯二甲酸盐含量 | 0221 | 2005/84/EC 欧盟关于邻苯二甲酸酯的指令内部方法 TP-C001 邻苯二甲酸酯的测试方法 |  | 测试方法为实验室自制方法 |
|  |  |  |  | 0221 | CPSIA Sec.108美国消费品安全促进法 CPSC-CH-C1001-9.3 邻苯二甲酸盐测定的标准操作程序 |  |  |
|  |  | 6 | 镍释放量 | 0202 | EN 1811:2011 用于测试来自与皮肤直接长久接触的产品上镍释放量的参考试验方法 |  |  |
|  |  |  |  | 0202 | EN 12472:2005+A1:2009 用模拟磨损和腐蚀的方法测试有涂层物品的镍释放 |  |  |
|  |  | 7 | 禁用偶氮染料含量 | 0224 | EN14362-1：2003+AC:2005纺织品.衍生自偶氮染色剂的特定芳香胺的测定方法.第1部分:未经萃取获得的特定偶氮染色剂使用的检测 |  |  |
|  |  |  |  | 0224 | 35 LMBG 82.02-2:2004 日用品分析 纺织日用品上使用某些偶氮染料的检测 |  |  |
|  |  |  |  | 0224 | EN 14362-2:2003+AC:2005纺织品-某些源自于偶氮染色剂的芳香胺的检测方法-第2部分：使用某些可萃取染料的偶氮色剂的测定 |  |  |
|  |  |  |  | 0224 | 35 LMBG 82.02-4:2004 日用品分析聚酯纤维上禁用偶氮染料的检测 |  |  |
|  |  |  |  | 0224 | 64 LFGB B 82.02-9:2006日用品测试方法－可释放出4－胺基偶氮苯的某些偶氮染料的验证 |  |  |
|  |  | 8 | 填充材料 | 0224 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.3.7填充材料， |  |  |
|  |  | 9 | DEHP | 0224 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.3.8DEHP |  |  |
|  |  | 10 | 亚硝胺 | 0224 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.20.1 亚硝胺 |  |  |
|  |  | 11 | 电性能 | 0327 | GB19865-2005/ IEC62115:2003/ EN 62115:2003 电玩具安全 |  |  |
|  |  | 12 | 色牢度 | 0327 | DIN53160-2002 着色玩具抗唾液和汗液测试 |  |  |
|  |  | 13 | 玩具标识和使用说明 | 0327 | GB5296.5-2006 消费品使用说明：玩具使用说明 |  |  |
|  |  |  |  | 0327 | ASTM F963-08 消费者安全规范：玩具安全 条款 4.30玩具枪标识 5 标识要求， 6 使用说明， 7 生产商标识， |  |  |
| 2 | 儿童推车 | 1 | 全部参数 | 0327 | EN1888:2003+A1:2005+A2:2005+A3:2005 儿童推车安全要求 |  |  |
| 3 | 婴儿学步车 | 2 | 全部参数 | 0327 | EN1273-2005 婴儿学步车安全要求 |  |  |

注：本表格仅作为表述方法格式示例，供相关人员参考。

# A.2英文表述示例

| № | Test Object | Item/Parameter | Code of Field | Title, Code of Standard or Method | Limitation | Note |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | № | Item/ Parameter |  |  |  |  |
| 1 | Toys Toys Toys Toys Toys Toys Toys Toys Toys Toys | 1 | Mechanical and physical properties | 0327 | GB6675-2003+A1:2005 Safety Technical code for toys |  |  |
|  |  |  |  |  | ISO 8124-1: 2009( E ) Safety of toys - Part 1: Safety aspects related to mechanical and physical properties AS/NZS ISO 8124.1:2002+ A1:2007 + A2:2009 Safety of toys - Part 1: Safety aspects related to mechanical and physical properties |  |  |
|  |  |  |  | 0327 | EN 71-1: 2011 Safety of toys - Part 1: Mechanical and physical properties BS EN 71-1:2011 Safety of toys - Part 1: Mechanical and physical properties |  |  |
|  |  |  |  | 0327 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section： 4.1 Material Quality， 4.5 Sound Producing Toys， 4.6 Small Objects， 4.7 Accessible Edges， 4.8 Projections， 4.9 Accessible Points， 4.10 Wires or Rods， 4.11 Nails and Fasteners， 4.12 Plastic Film， 4.13 Folding Mechanisms and Hinges， 4.14 Cords, Straps, and Elastics， 4.16 Confined Spaces， 4.17 Wheels, Tires, and Axles， 4.18 Holes, Clearances, and Accessibility of Mechanisms， 4.19Simulated Protective Devices， 4.20 Pacifiers， 4.21 Projectile Toys， 4.22 Teethers and Teething Toys， 4.23 Rattles， 4.24 Squeeze Toys， 4.26 Toys Intended to be Attached to a Crib or Playpen 4.27 Stuffed and Beanbag-Type Toys， 4.28 Stroller and Carriage Toys， 4.31 Balloons， 4.32 Certain Toys with Spherical Ends， 4.33 Marbles， 4.34 Balls， 4.35 Pompoms， 4.36 Hemispheric-Shaped Objects， 4.38 Magnets， 4.39 Jaw Entrapment in Handles and Steering Wheels， 8.5 Normal Use Testing， 8.6 Abuse Testing， 8.7 Impact Tests， 8.8 Torque Tests for Removal of Components试， 8.9 Tension Test for Removal of Components， 8.10 Compression Test， 8.11 Axle Assembly Removal， 8.12 Flexure Test， 8.14 Projectiles， 8.19 Tests for Toys which Produce Noise， 8.21 Packaging Film Thickness， 8.22 Test for Loops and Cords， 8.24 Magnet Test Methods， 8.25 Test Methods for Locking Mechanisms or Other Means （…………） |  |  |
|  |  | 2 | Flammability | 0327 | GB6675-2003+A1:2005 Safety Technical code for toys |  |  |
|  |  |  |  | 0327 | EN 71-2: 2011 Safety of toys - Part 2: Flammability | Except for Clause: 4.1 Flammable gases, extremely flammable liquids, high flammable liquids, flammable liquids & flammable gels. |  |
|  |  |  |  | 0327 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section： 4.2, Flammability， A5 Flammability Testing Procedure for Solids and Soft Toys， A6 Flammability Testing Procedure for Fabrics |  |  |
|  |  |  |  | 0327 | ISO 8124.3:2010 Safety of Toys –Part 3 Migration of certain elements |  |  |
|  |  | 3 | Migration of certain elements: Ba,As,Sb,Se,Cd,Pb,Cr,Hg | 0244 | AS/NZS ISO 8124-3:2003 Safety of Toys –Part 3 Migration of certain elements |  |  |
|  |  |  |  | 0244 | EN71-3:1994+A1:2000+AC:2002 Safety of toys-Part3:Migration of certain elements |  |  |
|  |  |  |  | 0244 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section： 4.3.5 Heavy Element 8.3 Test Methods for Determination of Heavy Element Content in Toys, Toy Components and Materials |  |  |
|  |  | 4 | Total lead content | 0215 | CPSC-CH-E1001-08.1 United States Consumer Product Safety Commission Directorate for Laboratory Sciences Division of Chemistry-Standard Operating Procedure for Determining Total Lead (Pb) in Children’s Metal Products (Including Children’s Metal Jewelry) |  |  |
|  |  |  |  | 0215 | CPSC-CH-E1002-08.1 United States Consumer Product Safety Commission Directorate for Laboratory Sciences Division of Chemistry-Standard Operating Procedure for Determining Total Lead (Pb) in Non-Metal Children’s Products |  |  |
|  |  |  |  | 0215 | ASTM E1613-04 Standard Test Method for Determination of Lead by Inductively Coupled Plasma Atomic Emission Spectrometry (ICP-AES), Flame Atomic Absorption Spectrometry (FAAS), or Graphite Furnace Atomic Absorpti on Spectrometry (GFAAS) Techniques |  |  |
|  |  |  |  | 0215 | ASTM E1645-07 Standard Practice for Preparation of Dried Paint Samples by Hotplate or Microwave Digestion for Subsequent Lead Analysis |  |  |
|  |  |  |  | 0215 | CPSC 16 CFR 1303 Product Safety Commission CPSC-CH-E1003-09.1 United States Consumer Product Safety Commission Directorate for Laboratory Sciences Division of Chemistry-Standard Operating Procedure for Determining Total Lead (Pb) in Paint and Other Similar Surface Coatings |  |  |
|  |  | 5 | Phthalates content | 0221 | 2005/84/EC DIRECTIVE OF THE EUROPEAN PARLIAMENT AND OF THE COUNCIL Laboratory-developed methods for Testing of Phthalates T-C001 |  | Laboratory-developed methods |
|  |  |  |  | 0221 | CPSC-CH-C1001-09.3 CPSIA Sec.108 Standard Operating Procedure for Determination of Phthalates |  |  |
|  |  | 6 | Nickel Release content | 0202 | EN 1811:2011 Reference test method for release of nickel from products intended to come into direct and prolonged contact with the skin |  |  |
|  |  |  |  | 0202 | EN 12472:2005+A1:2009 Method for the simulation of wear and corrosion for the detection of nickel release from coated items |  |  |
|  |  | 7 | AZO Dyes content | 0224 | EN14362-1：2003+AC:2005 Textiles-Methods for determination of certain aromatic amines derived from AZO colorants-Part 1:Detection of the use of certain AZO colorants accessible without extraction |  |  |
|  |  |  |  | 0224 | LMBG 82.02-2:2004 Examination of commodities :Determination of certain aromatic amines derived from AZO colorants in textiles35 |  |  |
|  |  |  |  | 0224 | EN 14362-2:2003+AC:2005 Textiles- Methods for determination of certain aromatic amines derived from AZO colorants-Part 2:Detection of the use of certain AZO colorants accessible by extracting the fibers |  |  |
|  |  |  |  | 0224 | 35 LMBG 82.02-4:2004 Examination of commodities :Determination of certain aromatic amines derived from AZO colorants in polyester |  |  |
|  |  |  |  | 0224 | 64 LFGB B 82.02-9:2006 Examination of commodities: Determination of 4-aminoazobenzene |  |  |
|  |  | 8 | Stuffıng Materials | 0224 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section 4.3.7 Stuffıng Materials， |  |  |
|  |  | 9 | DEHP | 0224 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section 4.3.8DEHP |  |  |
|  |  | 10 | Nitrosamine | 0224 | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section 4.20.1 Nitrosamine |  |  |
|  |  | 11 | Electric Safety | 0327 | GB19865-2005/ IEC62115:2003/ EN 62115:2005+A2:2011 Electric toys — Safety |  |  |
|  |  | 12 | Colorfastness | 0327 | DIN53160-2002 Resistance to Saliva and Perspiration |  |  |
|  |  | 13 | Label、 Mark & Instruction | 0327 | GB5296.5-2006 Instruction for use of products of consumer interest - Instruction for use of toys |  |  |
|  |  |  |  |  | ASTM F963-11 Standard Consumer Safety Specification for Toy Safety Section 4.30 Toy Gun Marking 5 Safety Labeling Requirements， 6 Instructional Literature， 7 Producer's Markings， |  |  |
| 2 | Wheeled child conveyances | 1 | All Parameter | 0327 | EN1888:2003+A1:2005+A2:2005+A3:2005 Child care articles - Wheeled child conveyances- Safety requirements and test methods |  |  |
| 3 | Baby walking frames | 2 | All Parameter | 0327 | EN 1273: 2005 Child use and care articles - Baby walking frames - Safety requirements and test methods |  |  |

注：本表格仅作为表述方法格式示例，供相关人员参考。